## Slide 1
DIGITAL DESIGN AND COMPUTER ARCHITECTURE
Design of a 4-Bit ALU Using Multiplexer
AND, OR and Set-Less-Than (SLT) Operations
Team Members: 2620030210 - Amulya
2620030208 - V.Vaishnavi
2620030209 - S.Akshaya
2620030205 - Jasmitha
Section: [S4 ]
Subject: Digital Design and Computer Architecture (DDCA)
Faculty Guide: Tanmoya mam
College Name: KLH

## Slide 2
PROJECT OVERVIEW
A 4-bit ALU combines three operations under one control interface
Supported operations
An Arithmetic Logic Unit is a CPU component that performs arithmetic and logical operations on binary data.
AND: bitwise logic on two 4-bit inputs.
OR: bitwise logic on two 4-bit inputs.
SLT: unsigned comparison of A and B.
A multiplexer selects the required result using two control signals, S1 and S0.
Project objectives
Design a 4-bit ALU using basic digital logic.
Implement AND and OR for two 4-bit inputs.
Compare unsigned 4-bit values using SLT.
Verify the circuit in Logisim or Logisim Evolution.
Design of a 4-Bit ALU Using Multiplexer
02

## Slide 3
CORE OPERATIONS
AND and OR are bitwise; SLT compares the full unsigned values
Each operation produces a 4-bit candidate result. The multiplexer later chooses which candidate reaches Y[3:0].
AND
Each output bit is 1 only when both corresponding input bits are 1.
Y[i] = A[i] AND B[i]
OR
Each output bit is 1 when at least one corresponding input bit is 1.
Y[i] = A[i] OR B[i]
Unsigned SLT
If A < B, output 0001; otherwise output 0000. SLT is a magnitude comparison, not a bitwise operation.
Operation selection
S1 | S0 | Selected operation | Output
0 | 0 | AND | A AND B
0 | 1 | OR | A OR B
1 | 0 | SLT | 0001 if A < B, otherwise 0000
1 | 1 | Reserved | Unspecified; do not use
Design of a 4-Bit ALU Using Multiplexer
03

## Slide 4
LOGISIM IMPLEMENTATION
Logisim implementation uses parallel logic and a 4-bit multiplexer
All candidate results are computed before the selected result is displayed.
Required components
Two 4-bit inputs: A[3:0] and B[3:0]
Four 2-input AND gates and four 2-input OR gates
One unsigned 4-bit magnitude comparator
Logic that converts A < B into 0001 or 0000
One 4-bit-wide 4-to-1 multiplexer
Two select signals, S1 and S0, and a 4-bit output Y[3:0]
Working sequence
Enter two 4-bit binary values.
Compute AND and OR results in parallel.
Compare A and B as unsigned values.
Form the four-bit SLT result.
Select the result with S1S0 and display Y[3:0].
Implementation placeholder: [INSERT GENUINE LOGISIM CIRCUIT SCREENSHOT HERE]
Reference only; complete implementation and verification in Logisim.
Design of a 4-Bit ALU Using Multiplexer
04

## Slide 5
Expected outputs are ready for verification in Logisim
For each test, S1S0 = 00 selects AND, 01 selects OR, 10 selects SLT, and 11 has no defined functional result.
Control selection
S1S0 | Operation
00 | AND
01 | OR
10 | SLT
11 | Reserved/Unused
Expected test cases — pending Logisim verification
Test | A | B | AND | OR | SLT
1 | 0101 (5) | 0011 (3) | 0001 | 0111 | 0000
2 | 0010 (2) | 0110 (6) | 0010 | 0110 | 0001
3 | 1111 (15) | 1111 (15) | 1111 | 1111 | 0000
4 | 0000 (0) | 0001 (1) | 0000 | 0001 | 0001
Simulation placeholder: [INSERT GENUINE LOGISIM SIMULATION SCREENSHOT HERE]
Design of a 4-Bit ALU Using Multiplexer
05

## Slide 6
CONCLUSION · FUTURE SCOPE
The design demonstrates combinational logic and controlled result selection
Conclusion
The conceptual 4-bit ALU supports AND, OR, and unsigned SLT.
Two control signals select the required result.
Logisim can be used for implementation and verification.
Applications
CPU and processor datapaths
Digital electronics and computer architecture education
Embedded-system learning
Future improvements
Addition and subtraction
XOR and NOT operations
8-bit or 16-bit inputs
Integration into a simple processor datapath

## Slide 7
Thank you